## Slide 1
HW/SW Co-Exploration to Enable Automated Machine Learning System Design
Frontiers of AI Accelerators: Technologies, Circuits and Applications II
Weiwen Jiang
wjiang8@gmu.edu
https://jqub.ece.gmu.edu

## Slide 2: Today, AI is Going to Every Embedded Computing Hardware
Agriculture
Military
Power System
Manufacture
Education
Medical Operation
Finance
……
Notes: Today, we expect that the computing can not only do the repeated jobs but also do these jobs smartly. That is, we would like to integrate intelligence in these systems to further reduce the burden on human beings.

## Slide 3: Bottleneck in Applying ML for Specific Applications
Ski
Manually Design Neural Network:
  Requires expertise from different domains
  Collaboration of these experts is difficult
  Large human labor
  Long launch time…
✔
Computer Vision Experts
Computer Scientist
Data Scientist
3

## Slide 4: AutoML is a Promising Solution
Action
Reward
e.g. Reinforcement Learning
Automated Design Neural Network:
  Replace exerts by using automated optimization approaches
  Release the labor from experts
  Short launch time
Ski
✔
Env.
4
    Objective:
    Maximize ML Performance
    (e.g., Prediction Accuracy)
Notes: == Until now, everything seems to be great, and the above bottlenecks have been addressed by Auto ML approaches and techniques.
Can you think about anything missed, or any problems? especially in these two applications about ML in Medical Imaging (Dermatology Diagnosis) and ML in Drug Discovery (Molecular Reaction and Toxic)

## Slide 5
AlexNet
ResNet
MobileNet
NASNet
Cloud / Server
  Unlimited Resource
  Maximizing Accuracy
  AlexNet, VGGNet, ResNet, …
Mobile Phones
  Fixed Hardware
  Accuracy v.s. Latency
  MnasNet, ProxylessNAS, …
Hardware Accelerators (e.g., FPGA)
  Hardware Design Flexibility
  Accuracy, Latency, and Energy
  FNAS, SkyNet, EDDNet…
MnasNet
ProxylessNAS
FBNet
SkyNet
FNAS
EDDNet
5
One Network Cannot Work for All Platforms
Notes: Now, I will show the importance of the second level of optimization. As shown in this slides, the intelligence is widely required in different computing platforms, such as cloud computing, mobile phones, and customized hardware accelerators. Different computing platforms have different requirements.
(click) For instance, the cloud computing have enough computing resources and the objective is to maximize accuracy.
(cick) For mobile phones, it has fixed hardware and a tradeoff between accuracy and latency needs to be made.
(click) For customized hardware, it further has hardware design flexibilities and it is expected to achieve better t’radeoffs among accuracy, timing performance and energy efficiency.
As a result, no uniform neural network architecture can work for all computing platforms. The existing works have explored different neural networks for different platforms, as shown in this slides.

## Slide 6
Neural Networks
Datasets / Applications
Hardware Platforms
FPGA
6
Problem: Datasets/Applications, Hardware, and Neural Networks
Notes: To better understand the following topics, now, let’s see the fundamental problem for the automation of AI system. As shown in this slides, we are given datasets, a specific hardware, and a search space of neural networks where each circle represent one potential neural network. We need to identify a neural network architecture from the search space, such that both software and hardware can achieve high performance.

## Slide 7: Outline
Background
A Quick Overview of The Road From Manual Design to AutoML
HW/SW Co-Exploration Framework
  Motivation
  Framework Overview and Details
  Results
Follow-up Works and Conclusion

## Slide 8: HW/SW Co-Exploration of Neural Architectures
Controller (RNN)
Train from Scratch
To Obtain Accuracy A
Sample architecture NN with probability p
Update controller by A
Neural Architecture Search (NAS)
HW-aware NAS
2016 - Now
2013
2012
2014
2015
2016
2017
2018
2019
2020
I. Human Invented
Aug. 2019
FNAS
FPGA/DNN (UIUC)
HW/CNN (Samsung)
II. NAS and HW-Aware NAS
MnasNet
from Google
proxylessNAS
from MIT
FBNet from UCB FB
HW/SW Co-Exploration
NANDS
NASAIC
III. HW/SW Co-exploration
AlexNet
ZFNet
VGGNet
GoogleNet
FPGA
ASIC
Network-on Chip
FPGA
ASIC
Computing-in-Mem
Neural Archi. Search (RL-based)
DARTS
SkyNet
EDD Net
2021
HW/SW Co-Exploration of Neural Architectures
Cloud/HPC
Mobile (Edge)
MCU (Tiny)
NACIM
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 9: Outline
Background
A Quick Overview of The Road From Manual Design to AutoML
HW/SW Co-Exploration Framework
  Motivation
  Framework Overview and Details
  Results
Follow-up Works and Conclusion

## Slide 10: Motivation
TABLE I
ON CIFAR-10 AND XILINX XC7Z015 FPGA: COMPARISONS OF THREE NEURAL ARCHITECTURE AND HARDWARE DESIGN PAIRS IN ACCURACY, THROUGHPUT, AND ENERGY EFFICIENCY (E.-E): A) OPTIMAL ARCHITECTURE ON A FIXED HARDWARE IMPLEMENTATION THROUGH HARDWARE-AWARE NAS; B) THE SAME ARCHITECTURE BUT WITH FURTHER FPGA OPTIMIZATION; AND C) A JOINTLY OPTIMIZED NEURAL ARCHITECTURE AND FPGA IMPLEMENTATION THROUGH OUR CO-EXPLORATION.
Hardware-Aware NAS (Fixed HW)
  Find network N under fixed HW H
Sequential Optimization:
  Find network N under fixed HW H
  Optimize HW H for N
Co-Exploration:
  Optimize N and H in one loop
  0.66% Accuracy Gain
  2.19X and 1.20X Throughput Gain
  2.27X and 1.40X Energy Efficiency
HW and Network Optimization are Coupled with Each Other
How to Co-Explore?
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 11: Framework: Optimizing Network Architecture and HW Design in One Loop
Optimization Controller
Evaluator
Search Space
SW
HW
Controller iteratively selects solution from the search space for evaluation
Controller is evolved using the evaluation results from previous iteration.
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 12: Framework: Optimizing Network Architecture and HW Design in One Loop
Evaluator
Search Space
SW
HW
Controller: Reinforcement learning based optimizer
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 13: Framework: Optimizing Network Architecture and HW Design in One Loop
Evaluator
Search Space Exploration:
  Network Hyperparameters (SW)
  Partition and Assignment (HW)
Controller
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 14: Framework: Optimizing Network Architecture and HW Design in One Loop
Evaluator:
  Obtain Accuracy A and HW Utilization U
  Generate Reward with A & U
Controller
Search Space
SW
HW
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 15: Framework: Optimizing Network Architecture and HW Design in One Loop
Controller iteratively selects solution from the search space for evaluation
Controller is evolved using the evaluation results from previous iteration.
Notes: Jan 2019 FNAS --(Ours)
April 2019 FPGA/DNN – UIUC
Aug 2019 HW/SW Co-exploration (Ours)
September2019 SkyNet -- U.S. National Security Agency
Dec 2019 NANDS – (Ours) – ASP-DAC20
Jan 2020 NASAIC -- Ours）-- DAC 2020
May2020 EDD Net -- Efficient Differentiable DNN Architecture and Implementation Co-search for Embedded AI Solutions

## Slide 16: Results
Pareto Frontier between Accuracy and HW Efficiency can be Significantly Pushed Forward
At most 2 FPGAs
At most 3 FPGAs

## Slide 17: Results
Minimizing model size may not achieve the highest hardware efficiency

## Slide 18: Results
Co-Exploration Outperform Competitors on Different Datasets

## Slide 19: Outline
Background
A Quick Overview of The Road From Manual Design to AutoML
HW/SW Co-Exploration Framework
  Motivation
  Framework Overview and Details
  Results
Follow-up Works and Conclusion

## Slide 20: Design Stack Built By the Team
HW/SW Co-Design Stack using NAS
  HW/SW Co-Design
  Quantum Machine Learning
Best Paper
Nominations:
Best Paper Award:

## Slide 21: Co-Design NAS Full-Stack
HW/SW
Co-Design
Framework
FNAS
[DAC’19*]
[TCAD’20*]
FPGA
XFER [CODES+ISSS’19*]
ASIC
NANDS [ASP-DAC’20*]
ASICNAS [DAC’20]
Computing-in-Memory
Device-Circuit-Arch.
[IEEE TC’20]
XFER:
Neural Network Partition
Performance Model
Multiple FPGA
Load Balance
Hardware
Best Paper Nomination

## Slide 22: Co-Design NAS Full-Stack
HW/SW
Co-Design
Framework
FNAS
[DAC’19*]
[TCAD’20*]
FPGA
XFER [CODES+ISSS’19*]
ASIC
NANDS [ASP-DAC’20*]
ASICNAS [DAC’20]
Computing-in-Memory
Device-Circuit-Arch.
[IEEE TC’20]
ASINAS:
Multi-Tasks
Template-Based NAS
Heterogenous ASICs
First HW/SW Co-Design
For ASICs with Huge
HW Design Space

## Slide 23: Co-Design NAS Full-Stack
HW/SW
Co-Design
Framework
FNAS
[DAC’19*]
[TCAD’20*]
FPGA
XFER [CODES+ISSS’19*]
ASIC
NANDS [ASP-DAC’20*]
ASICNAS [DAC’20]
Computing-in-Memory
Device-Circuit-Arch.
[IEEE TC’20]
NACIM:
Cross-layer Optimization
Multi-Object Optimization
CiM Accelerator
Device Variation
First HW/SW Co-Design
For Computing-in-Memory
Accelerators with
Device Variation

## Slide 24: Co-Design NAS Full-Stack
HW/SW
Co-Design
Framework
FNAS
[DAC’19*]
[TCAD’20*]
NAS Acc.
HotNAS [CODES+ISSS’20]
Model Compression
NAS for Quan. [ICCAD’19]
Compre.-Compilation [IJCAI’21]
Secure Infernece
NASS [ECAI’20]
BUNET [MICCAI’20]
More than 200  Less than 3 (GPU Hours) on ImageNet Dataset
Algorithm

## Slide 25: Co-Design NAS Full-Stack
HW/SW
Co-Design
Framework
FNAS
[DAC’19*]
[TCAD’20*]
Application
Medical Imaging
FaHaNA
Fairness
[DAC’22]
NAS for Medical Image Seg.
[MICCAI’20]
NLP (Transformer)
FPGA [ICCD’20]
Mobile [DAC’21]
GPU [GLSVLSI’21]
Graph-Based
Social Net [GLSVLSI’21]
Drug Discovery [ICCAD’21]
Melanoma
Basal cell carcinoma
Light Skin
76.80%
Dark Skin
49.38%
Fairness
Existing Networks
Vascular lesion
First Framework to Co-Optimize Accuracy and Fairness via NAS
DAC This Year!

## Slide 26: Co-Design NAS Full-Stack
HW/SW
Co-Design
Framework
FNAS
[DAC’19*]
[TCAD’20*]
Application
Medical Imaging
FaHaNA
Fairness
[DAC’22]
NAS for Medical Image Seg.
[MICCAI’20]
NLP (Transformer)
FPGA [ICCD’20]
Mobile [DAC’21]
GPU [GLSVLSI’21]
Graph-Based
Social Net [GLSVLSI’21]
Drug Discovery [ICCAD’21]
Algorithm
NAS Acc.
HotNAS [CODES+ISSS’20]
Model Compression
NAS for Quan. [ICCAD’19]
Compre.-Compilation [IJCAI’21]
Secure Infernece
NASS [ECAI’20]
BUNET [MICCAI’20]
Hardware
FPGA
XFER [CODES+ISSS’19*]
ASIC
NANDS [ASP-DAC’20*]
ASICNAS [DAC’20]
Computing-in-Memory
Device-Circuit-Arch.
[IEEE TC’20]

## Slide 27: Conclusion
The very first framework to conduct HW/SW co-exploration
Co-exploration can push forward Pareto frontier of accuracy vs. efficiency
Providing fundamentals of the co-design stack
We even apply the co-design philosophy to quantum machine learning, the initial work was published at Nature Communications

## Slide 28: Reference
[1] W. Jiang, J. Xiong, and Y. Shi, A Co-Design Framework of Neural Networks and Quantum Circuits Towards Quantum Advantage, Nature Communications, Jan. 2021
[2] W. Jiang, B. Xie, C-C Liu and Y. Shi, Integrating Memristors and CMOS for Better AI, Nature Electronics, Sep. 2019
[3] Y. Ding, W. Jiang, Q. Lou, J. Liu, J. Xiong, X. Sharon Hu, X. Xu, and Y. Shi, Hardware Design and the Competency Awareness of a Neural Network, Nature Electronics, Aug. 2020
[4] W. Jiang, E. H.-M. Sha, X. Zhang, L. Yang, Q. Zhuge, Y. Shi and J. Hu, Achieving Super-Linear Speedup across Multi-FPGA for Real-Time DNN Inference, International Conference on Hardware/Software Co-design and System Synthesis CODE+ISSS), also appears at ACM Transactions on Embedded Computing Systems (TECS), NYC, New York, USA, Oct. 2019. (BEST PAPER NOMINATION)
[5] W. Jiang, E. H.-M. Sha, Q. Zhuge, L. Yang, H. Dong and X. Chen, On the Design of Minimal-Cost Pipeline Systems Satisfying Hard/Soft Real-Time Constraints, IEEE International Conference on Computer Design (ICCD2017@BOSTON) & IEEE Transactions on Emerging Topics in Computing (TETC), Jan. 2018. (BEST PAPER AWARD)
[6] W. Jiang, L. Yang, E. H.-M. Sha, Q. Zhuge, S. Gu, S. Dasgupta, Y. Shi and J. Hu, Hardware/Software Co-Exploration of Neural Architectures, IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), Accepted, 2020.
[7] W. Jiang, E. H.-M. Sha, Q. Zhuge, L. Yang, X. Chen, and J. Hu, Heterogeneous FPGA-based Cost-Optimal Design for Timing-Constrained CNNs, International Conference on Compilers, Architecture, and Synthesis for Embedded Systems (CASES), also appears at IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), Torino, Italy, Oct. 2018.
[8] W. Jiang, E. H.-M. Sha, X. Chen, L. Yang, L. Zhou and Q. Zhuge, Optimal Functional-Unit Assignment for Heterogeneous Systems under Timing Constraint, IEEE Transactions on Parallel and Distributed Systems (TPDS), 28(9), 2567-2580, 2017.
28
Notes: Here is the list of my journal publications, including nature electionics, nature communications, and several IEEE and ACM transactions papers.

## Slide 29: Reference
[9] W. Jiang, E. H.-M. Sha, Q. Zhuge, L. Yang, X. Chen, and J. Hu, On the Design of Time-Constrained and Buffer-Optimal Self-Timed Pipelines, IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), Accepted, 2018.
[10] W. Jiang, L. Yang, S. Dasgupta, J. Hu and Y. Shi, Standing on the Shoulders of Giants: Hardware and Neural Architecture Co-Search with Hot Start, International Conference on Hardware/Software Co-design and System Synthesis CODE+ISSS), also appears at IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), Virtual, 2020.
[11] W. Jiang, Q. Lou, Z. Yan, L. Yang, J. Hu, X. S. Hu and Y. Shi, Device-Circuit-Architecture Co-Exploration for Computing-in-Memory Neural Accelerators, IEEE Transactions on Computers (TC), Accepted, 2020.
[12] E. H.-M. Sha, W. Jiang, H. Dong, Z. Ma, R. Zhang, X. Chen and Q. Zhuge, Towards the Design of Efficient and Consistent Index Structure with Minimal Write Activities for Non-Volatile Memory, IEEE Transactions on Computers (TC), 67(3), 432-448, 2018.
[13] W. Liu, L. Yang, W. Jiang, L. Feng, N. Guan, W. Zhang, and N. Dutt, Thermal-aware Task Mapping on Dynamically Reconfigurable Network-on-Chip based Multiprocessor System-on-Chip, IEEE Transactions on Computers (TC), Accepted, 2018.
[14] L. Yang, W. Liu, W. Jiang, M. Li, P. Chen and E. H.-M. Sha, FoToNoC: A Folded Torus-Like Network-on-Chip based Many-Core Systems-on-Chip in the Dark Silicon Era, IEEE Transactions on Parallel and Distributed Systems (TPDS), 28(7), 1905-1918, 2017.
[15] E. H.-M. Sha, X. Chen, Q. Zhuge, L. Shi and W. Jiang, A New Design of In-Memory File System Based on File Virtual Address Framework, IEEE Transactions on Computers (TC), 65(10), 2959-2972, Oct. 2016. (Editor’s pick of the year)
29

## Slide 30: Reference
[16] W. Jiang, J. Xiong, and Y. Shi, When Machine Learning Meets Quantum Computers: A Case Study," in Proc. of IEEE/ACM Asia and South Pacific Design Automation Conference (ASP-DAC), 2021 (Invited Paper)
[17] W. Jiang, X. Zhang, E. H.-M. Sha, L. Yang, Q. Zhuge, Y. Shi, and J. Hu, Accuracy vs. Efficiency: Achieving Both through FPGA-Implementation Aware Neural Architecture Search, Design Automation Conference (DAC), 2019 (BEST PAPER NOMINATION)
[18] L. Yang, W. Jiang, W. Liu, E. H.-M. Sha, Y. Shi and J. Hu, Co-Exploring Neural Architecture and Network-on-Chip Design for Real-Time Artificial Intelligence, Proc. Asia and South Pacific Design Automation Conference (ASP-DAC), Beijing, Jan. 2020. (BEST PAPER NOMINATION)
[19] L. Yang, Z. Yan, M. Li, H. Kwon, L. Lai, T. Krishana, V. Chandra, W. Jiang, and Y. Shi, Co-Exploration of Neural Architectures and Heterogeneous ASIC Accelerator Designs Targeting Multiple Tasks, Design Automation Conference (DAC), 2020.
[20] Q. Lu, W. Jiang, X. Xiao, J. Hu and Y. Shi, On Neural Architecture Search for Resource-Constrained Hardware Platforms, Proc. IEEE/ACM International Conference On Computer-Aided Design (ICCAD), Westminster, CO, 2019.
[21] B. Song, W. Jiang, Q. Lu, Y. Shi and T. Sato, NASS: Optimizing Secure Inference via Neural Architecture Search, Proc. European Conference on Artificial Intelligence (ECAI), Santiago de Compostela, June. 2020.
[22] W. Jiang, E. H.-M. Sha, Q. Zhuge, H. Dong and X. Chen, Optimal Functional Unit Assignment and Voltage Selection for Pipelined MPSoC with Guaranteed Probability on Time Performance, Proc. Languages, Compilers, and Tools for Embedded Systems (LCTES), Barcelona, Spain, Jun. 2017.
[23] W. Jiang , E. H.-M. Sha, Q. Zhuge and X. Chen, Optimal Functional-Unit Assignment and Buffer Placement for Probabilistic Pipelines, Proc. International Conference on Hardware/Software Co-design and System Synthesis (CODES+ISSS), Pittsburgh, PA, USA, Oct. 2016.
30
Notes: Here is a selected list of my conference publications.

## Slide 31
George Mason University
4400 University Drive Fairfax, Virginia 22030
Tel: (703)993-1000
wjiang8@gmu.edu