## Slide 1: Hardware/Software Co-Exploration of Neural Architectures on FPGAs
Weiwen Jiang
Postdoc Scholar
wjiang2@nd.edu
https://wjiang.nd.edu

## Slide 2
1
Introduction
XFER: Achieving Super-Linear Speedup across Multi-FPGA
- CODES+ISSS’19 (Best Paper Finalist)
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC’19 (Best Paper Finalist)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 3
Computation Demand > Supply
Performance density almost stops increasing
2
Number of DNN operations increases exponentially
[ref.1] Xu, Xiaowei, et al. "Scaling for edge inference of deep neural networks." Nature Electronics 1.4 (2018): 216.
[ref.2] Sutter, H. The free lunch is over: A fundamental turn toward concurrency in software. Dr Dobb’s J. 30, 202–210.

## Slide 4
Storage Demand > Supply
[ref.1] Xu, Xiaowei, et al. "Scaling for edge inference of deep neural networks." Nature Electronics 1.4 (2018): 216.
[ref.2] Sutter, H. The free lunch is over: A fundamental turn toward concurrency in software. Dr Dobb’s J. 30, 202–210.
Number of DNN parameters increases exponentially
Energy efficiency of memory almost stops increasing

## Slide 5
4
4
Neural Architecture Search
Neural Architecture Implementation on FPGAs
Efforts on Both Software and Hardware Sides are Required
Notes: Page 6:
Now, let’s move our eyesight to the other side of the bridge. I will introduce the progress of neural architecture search in the following.

## Slide 6
5
Introduction
XFER: Achieving Super-Linear Speedup across Multi-FPGA
- CODES+ISSS’19 (Best Paper Finalist)
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC’19 (Best Paper Finalist)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 7
Background

## Slide 8
FPGAs in DNN Applications
FPGA in Cloud Computing
[ref] Where Do FPGAs Stand in Auto IC Race? https://www.eetimes.com/document.asp?doc_id=1333419#
[ref] PYNQ on UAV http://brennancain.com/pynqcopter-an-open-source-fpga-overlay-for-uavs/
FPGA in Edge Computing
Notes: The workflow of deploying neural architecture on FPGA consists FPGA accelerator design, the HDL code generation, synthesis, place and routing, and hardware performance evaluation. Among these steps, in accelerator design and HDL code generation, hardware design knowledge is mandatory (click) . And for synthesis, and place&routing, (click)it can take dozens of hours. Such lengthy development can be an obstacle when Deploying Neural Architecture on FPGA. (click)

## Slide 9
[Ref] C. Zhang et al. Optimizing fpga-based accelerator design for deep convolutional neural networks. In Proc. of FPGA, pages 161–170. ACM, 2015.
Single-FPGA
Limited Resource  Limited Performance
[Ref] C. Zhang et al. Energy-efficient cnn implementation on a deeply pipelined fpga cluster. In Proc. of ISLPED, pages 326–331, 2016.
Pipelined FPGAs
Pipeline High Throughput
Latency is not improved
Response to Limited Resource: Pipelining Multi-FPGA
Notes: Multi-FPGA is a good solution to response to the limited resource.
In the early design stage, the single FPGA is applied to accelerate the DNN applications.
To increase hardware resource, it is naturally to employing multiple FPGAs to increase performance.
As shown in this slides, authors apply pipelining FPGAs to boost performance.

## Slide 10
Accelerator Design Parameter
Pipelining Multi-FPGA: Design Flow
Notes: We exam the design flow and made three observations.
We outline the design flow in this slides, where a convolutional neural network is given. And it will based on the pipelining idea to be partitioned into different pipeline stages, and map each stage to one FPGA.
To achieve the design, it is based on a performance model, which will determine the design parameters for the accelerator in each FPGA.
Then, the input DNN is divided to form the pipelining FPGAs.
In the following, let’s first see the accelerator design

## Slide 11
FPGA-based Acceleration
On-chip Memory cannot hold all data
Loop Tiling
Layer Parameters:
L=(B, M, N, R, C, K)
Tiling Parameters:
(Tm, Tn, Tr, Tc)
IFM
Weights
OFM
Tm
Tn
Tr
Tc
L
1
L
2
L
3
L
4
OFM
…
…
M
R
C
N
K
K
B
IFM
L2=
(
B, M, N, R, C, K
)
Layer Model
1
Batch Size (B)
# of OFM
Features Maps (M)
# of IFM
Feature Maps (N)
Row of IFM (R)
Column of IFM (C)
Kernel Size (K)
Accelerator Design Parameters
Notes: As shown in this slides, a convolution layer can be modeled using different parameters according to the activations and weigths.
For the accelerator design, activations and weights are initially stored in off-chip memory.
To execute the accelerator, data will be first moved to on-chip memory in FPGA. Then, computations are conducted in the FPGA to produce the output. Finally, the output will store to the off-chip memory.
However, during this process, due to the limited on-chip memory, we cannot move all data to FPGA once. As a result, loop tiling is proposed to only move partial data to the FPGA. And we can tile the activations and weights along different directions.
These tiling parameters are called design parameters.

## Slide 12
weights
128
…
192
13
13
…
…
128
13
13
Fig. Convolution of Layer 5 in AlexNet
Optimizations on design parameters
Observation:
Different design parameters lead to different performance
Design Parameters Will Significantly Affect the Performance
Notes: After we implement a convolution layer to one FPGA with different design parameters, we can obtain such a design space graph, where each point indicates a design. We have the observation here that different design parameters will lead different performance. Hence, it is important to optimize design parameters.

## Slide 13
Accelerator Design Parameter
Performance Model
Pipelining Multi-FPGA Design Flow
Notes: As shown in this slides, the determination of design parameters depend on the performance model. We next show the effects of performance model on optimizing designs.

## Slide 14
weights
128
…
192
13
13
…
…
128
13
13
Fig. Convolution of Layer 5 in AlexNet
Fig. Real Performance of Layer 5 in Alexnet on ZCU 102
Best model performance
Best real performance
(leads to sub-optimal solution)
Observation:
Inaccurate performance model for multi-FPGA
Without fine-grained memory access model and inter-FPGA communication model
Inaccurate Performance Model Leads to Sub-Optimal Design
Notes: As shown in this slides, after we implementing two specific designs, A and B onto the Xilinx board. We observe that the existing performance model without fin-grained communication model is inaccurate. In addition, we observe that the best model performance will not be the best real performance. This indicates that the inaccurate model will lead to the sup-optimal solution.

## Slide 15
Accelerator Design Parameter
Performance Model
Pipelining Design
Will Increase Latency
Traffic Surveillance
Self-Driving Vehicle
Robots in Surgery
[ref.1] Google’s Waymo
[ref.2] da Vinci Surgical Robot at St. Francis Health Center - Robotic Gizmos
Pipelining Multi-FPGA Design Flow
Notes: Finally, let’s review the pipelining design. Such a design can improve throughput benefiting from multiple FPGAs, but it cannot improve and even degrade the latency. On the other hand, the current applications mainly have the real-time requirement. In consequence, we need innovations in multi-FPGA design.

## Slide 16
[Ref] C. Zhang et al. Optimizing fpga-based accelerator design for deep convolutional neural networks. In Proc. of FPGA, pages 161–170. ACM, 2015.
Single-FPGA
Limited Resource  Limited Performance
[Ref] C. Zhang et al. Energy-efficient cnn implementation on a deeply pipelined fpga cluster. In Proc. of ISLPED, pages 326–331, 2016.
Pipelined FPGAs
Pipeline High Throughput
Latency is not improved
Response to Limited Resource: Pipelining Multi-FPGA
Weight Locking based Multi-FPGA
Lock weights to multiple FPGAs  Specific for RNN
Not applicable for sharing weights (e.g. CNN)
[Ref] Eric Chung, et al. Serving DNNs in Real Time at Datacenter Scale with Project Brainwave, In IEEE Micro, 2018
Notes: Multi-FPGA is a good solution to response to the limited resource.
In the early design stage, the single FPGA is applied to accelerate the DNN applications.
To increase hardware resource, it is naturally to employing multiple FPGAs to increase performance.
As shown in this slides, authors apply pipelining FPGAs to boost performance.

## Slide 17
Super-LIP Framework

## Slide 18
Super-LIP Framework
XFER Design
Targeting on Minimizing Latency
Optimizing Design Parameters with a more Accurate Model
Accelerator Design
XFER Design
Notes: First, we propose a novel XFER design that targets on minimizing latency.
Second, we proposed a optimization model which can accurately predict the latency of a given design. In addition, the model can support the proposed XFER design with multiple FPGAs.

## Slide 19
Optimizing Design Parameters with a more Accurate Model
Accelerator Design
XFER Design
Super-LIP Framework
XFER Design
XFER Design
Targeting on Minimizing Latency

## Slide 20
XFER Design

## Slide 21
Performance on Single FPGA bounded by Limited Resource
FPGA 1
FPGA 2
IFM
Weights
OFM
NN | Operation | Cycles | Note
AlexNet Layer 5 | Comm_IFM | 2,612 | Performance Dominated by Comm_Weights Latency is 5,658
 | Comm_Weights | 5,658 | 
 | Comm_OFM | 368 | 
 | Computation | 3,326 | 
K times
(in terms of tiling parameters)
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 22
FPGA 1
FPGA 2
Double Computation Resource cannot Double Performance
NN | Operation | Single | w/o XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 |  | 
 | Comm_Weights | 5,658 |  | 
 | Comm_OFM | 368 |  | 
 | Computation | 3,326 |  | 
Partition
for
Parallel
w/o XFER
1,412
2,953
234
1,782
IFM
Weights
OFM
K times
(in terms of tiling parameters)
Note
1.91X Speedup
times
(K is in terms of tiling parameters)
(m is in terms of stride and padding)
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 23
FPGA 1
FPGA 2
XFER: Achieve Super-Linear Speedup by Transferring Accesses —— from Off-Chip Memory to Inter-FPGA Links
NN | Operation | Single | w/o XFER | w/ XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 | 1,412 |  | 
 | Comm_Weights | 5,658 | 2,953 |  | 
 | Comm_OFM | 368 | 234 |  | 
 | Computation | 3,326 | 1,782 |  | 
XFER
Further Partition
Weights
Note
Bottleneck Moves to Comp. 3.18X Speedup
w/ XFER
1,412
1,695
234
1,782
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 24
Application Optimization —— Partitioning
XFER Design
Weight Sharing: (Pb, Pr, Pc)
IFM Sharing: (Pm)

## Slide 25
Performance Model

## Slide 26
XFER Design
Targeting on Minimizing Latency
Super-LIP Framework
XFER Design
Optimizing Design Parameters with a more Accurate Model
Accelerator Design
XFER Design

## Slide 27
Accelerator Design —— On-Chip Design
Accelerator Design —— Accurate Model
Computation (MACs):
Communication Parameters (bit/cycle):
Ip: bandwidth for loading IFM
Wp: bandwidth for loading weights
Op: bandwidth for storing OFM
Accelerator Model
OFM Stationary Data Flow

## Slide 28
Accelerator Design —— Optimization under Resource Constraints
Accelerator Design —— Accurate Model
Computation (MACs):
Communication Parameters (bit/cycle):
Ip: bandwidth for loading IFM
Wp: bandwidth for loading weights
Op: bandwidth for storing OFM
Given:
Layer (B, M, N, R, C, K)
Computation resource — DSP ()
On-chip memory size ()
Off-chip memory bandwidth ()
Determine:
Tiling: (Tm, Tn, Tr, Tc)
Bandwidth allocation: (Ip, Wp, Op)
Partition: (Pb, Pr, Pc, Pm)
Objective:
Minimizing latency under resource constraints
Problem Definition
Computation Resource Constraint
Computation(32-bit): ; or (16-bit) ;
IFM buffer:
Weight buffer:
OFM buffer:
bitwidth(32b or 16b)
BRAM blokc size
Memory Resource Constraints
Communication Resource Constraint
OFM Stationary Data Flow

## Slide 29
Accelerator Design —— Optimization under Resource Constraints
Accelerator Design —— Accurate Model
Computation (MACs):
Communication Parameters (bit/cycle):
Ip: bandwidth for loading IFM
Wp: bandwidth for loading weights
Op: bandwidth for storing OFM
Given:
Layer (B, M, N, R, C, K)
Computation resource — DSP ()
On-chip memory size ()
Off-chip memory bandwidth ()
Determine:
Tiling: (Tm, Tn, Tr, Tc)
Bandwidth allocation: (Ip, Wp, Op)
Partition: (Pb, Pr, Pc, Pm)
Objective:
Minimizing latency under resource constraints
Problem Definition
Computation:
Load IFM:
Load Weight:
Store OFM:
Memory Access and Computation Latency
Latency under Parallelism: OFM stationary
Lat1
Lat2
Lat
Inner most para:
Second layer para:
Total Latency:
Pipeline loading time
# of loops
OFM Stationary Data Flow

## Slide 30
XFER Design —— Weight Sharing
XFER Design
Model Modifications:
Load Weight:
Inner most para:
Inter-FPGA latency:

## Slide 31
XFER Design —— IFM Sharing
XFER Design
Model Modifications:
Inner most para:
Inter-FPGA latency:
Load IFM:

## Slide 32
XFER Design —— Scale-Up
XFER Design
Topology: 2D-torus
Data Movement: Pipelining
Example:
&

## Slide 33
XFER Design
Targeting on Minimizing Latency
Recap —— Super-LIP Framework
XFER Design
Optimizing Design Parameters with a more Accurate Model
Accelerator Design
XFER Design

## Slide 34
Model Overview
Accelerator Design —— Accurate Model
Computation:
Load IFM:
Load Weight:
Store OFM:
2. Memory Access and Computation Latency
3. Parallelism (Pipelining and Double Buffer)
Lat1
Lat2
Lat
Inner most para:
Second layer para:
Total Latency:
1. Resource Constraints
Computation(32-bit): ; or (16-bit) ;
IFM buffer:
Weight buffer:
OFM buffer:
4. Communication among Multiple FPGAs (XFER)
Objective:
Transfer Weights:
Transfer IFM:

## Slide 35
Results

## Slide 36
Testbed:
CNN: AlexNet
FPGA: Xilinx ZUC102 FPGAs connected by SFP+ Links
XFER
Lowest
Latency
among all
competitors
Comparison results of XFER with comparisons to GPUs and the existing FPGA designs
Comparison with Existing Designs and GPU Platforms
Notes: Page 22:
Finally, we conduct experiments on Xilinx ZCU102 boards.
Compared with GPU and the existing FPGA implementations, we can see that XFER can achieve the lowest latency.

## Slide 37
Comparison results of XFER with SOTA single FPGA design
Achieve Super-Linear Speedup for both 32-bits and 16-bits implementations
Comparison with Single-FPGA Design on ZCU102 Boards
Notes: Page 23:
Compare with the single-FPGA design, we can see that we can achieve more than 2 times speedup with 2 FPGAs.

## Slide 38
Model Accuracy Evaluation
Ours: average deviation is only 2.53%
Existing model: deviation is up to 45.47%
We can accurately estimate performance of multiple FPGAs
Performance Bottleneck Detection and Alleviation using the proposed model

## Slide 39
https://github.com/PITT-JZ-COOP/XFER_FPGA
Performance Model
XFER Design
  HLS
  SDK
  Vivado_project
Open Source

## Slide 40
39
Introduction
XFER: Achieving Super-Linear Speedup across Multi-FPGA
- CODES+ISSS’19 (Best Paper Finalist)
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC’19 (Best Paper Finalist)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 41
40
40
Neural Architecture Search
Neural Architecture Implementation on FPGAs
Efforts on Both Software and Hardware Sides are Required
Notes: To maximize the energy efficiency, starting from 2015, a lot of works are carried out to implement a fixed architecture on FPGA.
However, with the growing demands on real-time AI, it is more critical to improve the timing performance of FPGA accelerators, which are usually bounded by the limited resource on one FPGA.
To response to this problem, there is trend to involve multiple FPGAs to implement deep neural networks.
But, it still lacks a design to efficiently utilize multiple FPGAs. Our transfer work aims to address this problem.
On the other hand, in the last 2 years, there are sharply increasing number of works targeting on neural architecture search. This has already become a very hot topic.
However, there is still a missing link between the neural architecture search and FPGA-implementation, so how do we search for neural architecture that works best for FPGA is still unknown.
Our FNAS work aims to propose a co-exploration framework to fill this gap.
In the following, I’ll introduce the backgrounds on FPGA-implementation side and Neural Architecture Search side in turn.

## Slide 42
2013
2012
2014
2015
2016
2017
2018
2019
AlexNet
GoogLeNet
VGGNet
ZFNet
2020
I. Human
Invented
II. Pure Automatically Explore Neural Architecture Space
III. Hardware-Aware
Neural Architecture Search
2018.Nov
proxylessNAS
from MIT
2018.Dec
FBNet
from UCB & Facebook
2019
2018.July
MnasNet
from Google
Neural Architecture Search (RL-based)
Evolution of Exploring Deep Neural Architectures
Notes: We can divide the evolution of exploring neural architectures in four stages.
The first stage is human invented stage, in which neural architectures are manually explored by experts, however, it requires large expertise and labor. (click)
Then, in the second stage, neural architecture search algorithms is proposed to automatically identify architectures. It release the expertise but can easily become useless since their structures are too complicated and cannot satisfy the timing performance. (click)
The third stage is the hardware-aware neural architecture search, which involve the hardware-efficiency in the search loop. (click)
Finally, our FNAS work pushes the exploration to the fourth stage, which will co-explore neural architecture and hardware design.
In the following slides, I will introduce each stage in detail and show the motivation of the co-exploration.

## Slide 43
VGGNet
AlexNet
……
Domain knowledge and excessive labor
It is impossible to manually design specific arch. for dedicated application in the era of AI democratization
Problem
Design arch. for dedicated application
Era of AI Democratization
Phase I: Human Invented
Notes: In the first stage, the neural network architectures are designed for the dedicate applications and dataset; for instance, the AlexNet and VGGNet are designed for image classification application on ImageNet dataset. (click)
However, when it comes to the era of AI democratization, there are exponentially growing number of applications. As a result, it is impossible to manually design architectures for each application.

## Slide 44
Intelligent Edge with Limited Computing Power
Controller (RNN)
Train a child network with architecture
NN to get accuracy A
Sample architecture NN with probability p
Compute gradient of p and scale it by A to update the controller
REF: Zoph, Barret, and Quoc V. Le. "Neural architecture search with reinforcement learning." ICLR 2017
before convergence
after convergence
Intelligent Cloud
with Enough Computing Power
No constraint on hardware resource consumed
NAS may not meet the design specifications in resource constraint environment
Problem
Identified
NN
Phase II: Neural Architecture Search (NAS)
Notes: In such background, the neural architecture search algorithms are proposed to automatically identify the architecture.
The NAS is typically implemented as a search loop, which composed of two components: a controller and a trainer.
The controller will predict the hyperparameters to identify an architecture. And the architecture will be then trained from scratch to obtain the accuracy. Then the accuracy will be feedback to update controller with the objective of maximizing the accuracy. (click)
We observe that the network explored by NAS has complicated structures, which is fine for the cloud computing with enough computing power. (click)
But, when it comes to edge computing, which commonly has limited resource and tight hardware specifications (such as latency and throughput), if we directly implement the identified architectures onto the edge devices, it is easily violate the specification and result in the architecture useless.

## Slide 45
Controller (RNN)
Train a child network with architecture
NN to get accuracy A
Sample architecture NN with probability p
Compute gradient of p and scale it by A and E to update the controller
REF: Mingxing Tan, et al. "MnasNet: Platform-Aware Neural Architecture Search for Mobile.” arXiv 2018
Predict the efficiency E on a fixed hardware (e.g. mobile phone)
It works for particular fixed hardware, but not suitable for programmable hardware
Problem
Different Hardware Designs
Phase III. Hardware-Aware NAS
Notes: To solve this problem, hardware-aware NAS is proposed, which adds an extra component in the search loop as shown in this slide.
It will test the hardware efficiency after training the neural network. (click)
In this way, the hardware efficiency can be guaranteed, but it increases the latency of search process. (click)
What’s more, it only works for fixed hardware, but not suitable for the programmable hardware.

## Slide 46
A Missing Link between Two Design Spaces
Neural Architecture Search
Neural Architecture Implementation on Hardware
Notes: Although two design spaces have been well explored, there is a missing link between these two spaces.
What’s more, we observe that these two spaces are tightly coupled, separately optimization will lead to inferior solutions.
Therefore, it is best to jointly explore these two spaces.
FNAS is proposed to remedy this gap.

## Slide 47
2013
2012
2014
2015
2016
2017
2018
2019
AlexNet
GoogLeNet
VGGNet
ZFNet
2020
I. Human
Invented
II. Pure Automatically Explore Neural Architecture Space
III. Hardware-Aware
Neural Architecture Search
2018.Nov
proxylessNAS
from MIT
2018.Dec
FBNet
from UCB & Facebook
2019
2018.July
MnasNet
from Google
Neural Architecture Search (RL-based)
DAC19 FNAS
from ND
IV. Co-Explore Neural Architecture Space
and Hardware Design Space
……
Evolution of Exploring Deep Neural Architectures
Notes: We claim that, the proposed FNAS pushes the neural architecture evolution into the fourth stage, that is, co-exploration stage.

## Slide 48
FNAS Framework

## Slide 49
Output: A pair of neural architecture and hardware design
FNAS
HW-Aware NAS vs. FPGA-Implementation Aware NAS（FNAS）
Output: A neural architecture
HW-Aware NAS
Notes: We first show the difference between the co-exploration framework with the existing hardware-aware NAS.
As stated, the hardware-aware NAS integrated a component to test the accuracy for each child network. It finally outputs a neural architecture with high accuracy. (click)
Unlike this framework, our proposed co-exploration framework is composed of two levels of exploration.
The top layer shows the hardware exploration level, and the bottom layer shows the software exploration level.
There are two controllers cooperatively explore neural architecture and hardware implementation.
As shown in this slides, after the controller for maximizing accuracy generate a child network, our framework can also test its hardware efficiency. If it cannot meet specifications, we can terminate the training early to reduce search time. Otherwise, it applies the latency and accuracy together to update the controller.
Then, the parameters of the controller is copied to the other controller. And it optimizes the hardware implementation with the objective of maximizing hardware efficiency.

## Slide 50
Naïve Solution: HW-Aware + Exhaustively Evaluate Lat.
Challenges:
Functional Spec.
HDL
Synthesis
Place & Route
HW Evaluation
Fig2. Procedure of performance evaluation
C3: Time-consuming evaluation!
Our Solution: FNAS tools to response to challenges
C2: Multi-FPGA design!
C1
C2
C2
C3
Fig1. Possible designs for Layer 5 of AlexNet on ZCU102
C1: Huge design space!
Infeasible
Solutions & Challenges
Exhaustively
Evaluate
Latency
FNAS
Tool
Notes: The naïve solution is to apply hardware-aware approach and exhaustively evaluate performance.
However, it faces a lot of challenges which leads such approach infeasible.
First, it has huge design space. As shown in the figure, each point in the graph represent one possible design, and the design space is huge.
Second, when we consider multiple FPGAs, the design space increases exponentially.
Finally, if we do not have automatic approach to evaluate performance, it is time-consuming.
To address these challenges, we propose the FNAS toolset, which contains four components.

## Slide 51
REF: Chen Zhang et al. 2015. Optimizing fpga-based accelerator design for deep convolutional neural networks. In Proc. of FPGA.
1. FPGAs with attributes including DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
On-chip accelerator design:
1. On-chip buffer allocation; 2. Accelerator size for computing
(note: both are determined by tiling parameters, Tm, Tn, Tr, Tc)
Determine：
One layer:
Multiple layers:
FNAS: Design Optimization (on-chip design)
Tn/Tm
Tn/Tm
Notes: The first component is the FNAS-Design. It determine the on-chip buffer size, and accelerator size.
These parameters are affected by tiling parameters. And we have an automatic algorithm to help to determine best parameters given an architecture.

## Slide 52
High-level graph abstraction
1. FPGAs with attributes including DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
FNAS: Graph Generator
Notes: The second component is the graph generator. It bases the tiling results to abstract a graph model for the neural network.

## Slide 53
1. FPGAs with attributes including DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
Schedule of tasks in graph on multiple FPGAs
FNAS: Schedule (off-chip design)
Notes: Based on the graph model, we build a scheduler to determine the execution order of each operation.

## Slide 54
Latency = pipeline start time + processing time
1. FPGAs with attributes including DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
1. A tailored FPGA Design
2. The system latency
Output：
FNAS: Analyzer
Notes: Finally, we based on our FPGA performance model studied in the previous work to efficiently analyze the performance without simulation.

## Slide 55
Experimental Results
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 56
MNIST
CIFAR-10
ImageNet
Datasets
NAS Search Space
Layer Num.
Filter Size
Filter Num.
Channel Tiling Para. (Tm,Tn); Row Tiling Para. (Tr); Col Tiling Para. (Tc); Schedule
up to 5
up to 10
up to 15
[5, 7, 14]
[1, 3, 5, 7]
[1, 3, 5, 7]
[9, 18, 36]
[24, 36, 48, 64]
[16, 32, 64, 128]
[2, 5, 10, 20]
[1.5, 2, 2.5, 10]
[2.5, 5, 7.5, 10]
FPGAs
Xilinx 7A50T
Xilinx 7Z020
HW Search Space
Timing Spec. (ms)
Experimental Setting
Notes: In the experiments, we use different FPGAs to composed the hardware design space.
For the architecture search space, we specify number of layers, filter sizes, and filter numbers for different dataset, including MNIST, CIFAR-10 and ImageNet.
We also test using different timing specifications.

## Slide 57
up to 11.13X reduction in search time
up to 7.81X reduction in inference latency
below 0.9% loss in accuracy
Different Hardware (MNIST)
Different Datasets (7Z020)
Compare to HW-Aware NAS
(CIFAR-10 + 7Z020)
FNAS can significantly push forward the Pareto frontiers between accuracy and efficiency tradeoff
below 1% loss in accuracy
up to 10X reduction in inference latency
Baseline: NAS
loose
Experimental Results
Notes: We conduct experiments on different hardware and datasets. We also compare FNAS with original NAS and hardware-aware NAS.
As shown in the first group of experiments, where the x-axis represent different FPGAs, and y-axis represent search time, latency, and accuracy. We can see that FNAS can achieve 11 times reduction on search time, and 7 times reductions on latency, with only 0.9 percent accuracy loss.
For different datasets, we can obtain similar results.
Finally, we show that FNAS can significantly push forward the Pareto frontiers between accuracy and efficiency tradeoff.

## Slide 58
Experimental Results: Importance of Co-Exploration
Model Size
149k ~ 150k
Hardware Efficiency
7.02% ~ 98.53%
In the design space:
Models with similar model sizes may have distinct hardware efficiency
=> Cannot restrict model size to guarantee hardware efficiency

## Slide 59
58
Introduction
XFER: Achieving Super-Linear Speedup across Multi-FPGA
- CODES+ISSS’19 (Best Paper Finalist)
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC’19 (Best Paper Finalist)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 60
59
59
Our Work on Co-Exploring Neural Architecture and Hardware
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)

## Slide 61
60
60
Our Work on Co-Exploring Neural Architecture and Hardware
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability (multiple-FPGAs, NoCs, etc.)
Limited Resource (quantization, etc.)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
……

## Slide 62
61
61
Design Neural Networks on Scalable Architecture
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Super-Linear Speedup across Multiple FPGAs (XFER)
CODES+ISSS’19
Best Paper Nomination
ASP-DAC’20
Best Paper Nomination
Co-Explore Network-on-Chip Design and Neural Architectures (NANDS)

## Slide 63
62
62
Design Neural Networks for Resource-Limited Device
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Limited Resource in Edge Computing (quantization, etc.)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
……

## Slide 64
63
63
Design Neural Networks for Resource-Limited Device
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Limited Resource in Edge Computing (quantization, etc.)
ICCAD’19
Co-Explore Quantization and Neural Architectures (QuanNAS)

## Slide 65
64
64
Design Neural Networks for Novel Computing Architectures
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Limited Resource in Edge Computing (quantization, etc.)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
……

## Slide 66
65
65
Design Neural Networks for Novel Computing Architectures
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
Integrating Memristors and CMOS for Better AI
Nature Electronics’19
Ongoing Project
Co-Explore Neural Architectures and Devices

## Slide 67
66
Introduction
XFER: Achieving Super-Linear Speedup across Multi-FPGA
- CODES+ISSS’19 (Best Paper Finalist)
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC’19 (Best Paper Finalist)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 68
Conclusion and Future Work
FNAS
Neural Network
Architecture
Search
Large Scale System
for Real-Time AI
FNAS
AI Democratization
XFER
NANDS
QuanNAS
?
?
New
Architectures
(ASIC, NVM, …)

## Slide 69
68
[1] Weiwen Jiang, Xinyi Zhang, Edwin H.-M. Sha, Qingfeng Zhuge, Lei Yang, Yiyu Shi and Jingtong Hu, "Accuracy vs. Efficiency: Achieving Both through FPGA-Implementation Aware Neural Architecture Search," in Proc. of DAC 2019. (Best Paper Finalist)
[2] Weiwen Jiang, Edwin Sha, Xinyi Zhang, Lei Yang, Qingfeng Zhuge, Yiyu Shi and Jingtong Hu, "Achieving Super-Linear Speedup across Multi-FPGA for Real-Time DNN Inference," CODES+ISSS 2019 and ACM TECS (Best Paper Finalist)
[3] Lei Yang, Weiwen Jiang, Weichen Liu, Edwin Sha, Yiyu Shi and Jingtong Hu, "Co-Exploring Neural Architecture and Network-on-Chip Design for Real-Time Artificial Intelligence," ASP-DAC 2020 (Best Paper Finalist)
[5] Qing Lu, Weiwen Jiang, Xiaowei Xu, Yiyu Shi and Jingtong Hu, "On Neural Architecture Search for Resource-Constrained Hardware Platforms," in Proc. of ICCAD 2019 (Invited Paper)
[6] Weiwen Jiang, Bike Xie, Chun-Chen Liu and Yiyu Shi, "Integrating Memristors and CMOS for Better AI," Nature Electronics, September 2019
Reference

## Slide 70: Thank You!
Weiwen Jiang
wjiang2@nd.edu
https://wjiang.nd.edu

## Slide 71
FPGA 1
FPGA 2
XFER: Achieve Super-Linear Speedup by Transferring Accesses —— from Off-Chip Memory to Inter-FPGA Links
NN | Operation | Single | w/o XFER | w/ XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 |  |  | 
 | Comm_Weights | 5,658 |  |  | 
 | Comm_OFM | 368 |  |  | 
 | Computation | 3,326 |  |  | 
XFER
Note
Bottleneck Moves to Comp. 3.18X Speedup
w/ XFER
1,412
1,695
234
1,782
w/o XFER
1,412
2,953
234
1,782
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 72
XFER: Architecture and Motivation
FPGA 1
FPGA 2
Different clock domains for computation (low) and communication (high)
Communication not go through Off-Chip Memory, but directly switch between on-chip buffers
Feature
Results & Motivations
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 73
Performance on Single FPGA bounded by Limited Resource
FPGA 1
FPGA 2
IFM
Weights
OFM
NN | Operation | Cycles | Note
AlexNet Layer 5 | Comm_IFM | 2,612 | Performance Dominated by Comm_Weights Latency is 5,658
 | Comm_Weights | 5,658 | 
 | Comm_OFM | 368 | 
 | Computation | 3,326 | 
K times
(in terms of tiling parameters)
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 74
FPGA 1
FPGA 2
Double Computation Resource cannot Double Performance
NN | Operation | Single | w/o XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 |  | 
 | Comm_Weights | 5,658 |  | 
 | Comm_OFM | 368 |  | 
 | Computation | 3,326 |  | 
Partition
for
Parallel
w/o XFER
1,412
2,953
234
1,782
IFM
Weights
OFM
K times
(in terms of tiling parameters)
Note
1.91X Speedup
times
(K is in terms of tiling parameters)
(m is in terms of stride and padding)
Loading IFM, OFM, Computation are conducted independently on two FPGAs
Performance is still dominated by loading weights, and weights are duplicated on two FPGAs
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 75
FPGA 1
FPGA 2
XFER: Achieve Super-Linear Speedup by Transferring Accesses —— from Off-Chip Memory to Inter-FPGA Links
NN | Operation | Single | w/o XFER | w/ XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 | 1,412 |  | 
 | Comm_Weights | 5,658 | 2,953 |  | 
 | Comm_OFM | 368 | 234 |  | 
 | Computation | 3,326 | 1,782 |  | 
XFER
Further Partition
Weights
Note
Bottleneck Moves to Comp. 3.18X Speedup
w/ XFER
1,412
1,695
234
1,782
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 76
Experimental Results
Testbed:
Xilinx ZUC102 FPGAs connected by SFP+ Links
XFER
Lowest
Latency
among all
competitors
Comparison results of XFER with comparisons to GPUs and the existing FPGA designs
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 77
Experimental Results
Comparison results of XFER with SOTA single FPGA design
Achieve Super-Linear Speedup for both 32-bits and 16-bits implementations
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 78
Real-Time Requirement
[ref.1] Google’s Waymo
[ref.2] da Vinci Surgical Robot at St. Francis Health Center - Robotic Gizmos
Self-Driving Vehicle
Traffic Surveillance
Increasing Demands on Real-Time Machine Learning Applications
Robots in Surgery

## Slide 79
Experimental Results: Superior to Existing Approaches
Optimizing Network Accuracy
Comparison the proposed Co-Exploration with Hardware-Aware NAS and Heuristic Sequential Optimization
n
Optimizing Hardware Efficiency

## Slide 80
D,E,F are explored by our Co-Exploration framework, which output
QuanNAS: Co-Explore Quantization and Neural Architectures
D
Search Space
Besides filter size and shape, we co-explore bit width of weights and activation data, for FPGAs and ASICs.
D
Results
A,B are first explored by NAS, then to be quantized. In this way, the accuracy loss by quantization is huge.
D,E,F are explored by our Co-Exploration framework, which output better accuracy for quantized network with smaller parameter size

## Slide 81
NANDS: Co-Explore NoC Design and Neural Architectures
D
Why NoC? Complicated Structure from NAS
Fixed design (X-Y routing) leads lower performance
31.37% Improvement
D
Co-Exploration Framework
Results

## Slide 82
[1] Chen Zhang, et al. Optimizing fpga-based accelerator design for deep convolutional neural networks. In FPGA, 2015.
[2] Chen Zhang, et al. Energy-efficient cnn implementation on a deeply pipelined fpga cluster. In ISLPED, 2016.
[3] Chen Zhang, et al. Caffeine: Towards uniformed representation and acceleration for deep convolutional neural networks. ICCAD, 2016.
[4] Yongming Shen, et al. Maximizing cnn accelerator efficiency through resource partitioning. In ISCA, 2017.
[5] Eric Chung, et al. Serving dnns in real time at datacenter scale with project brainwave. IEEE Micro, 2018.
[6] Jeremy Fowers, et al. A configurable cloud-scale dnn processor for real-time ai. In ISCA, 2018.
[7] Weiwen Jiang, et al. Heterogeneous fpga-based cost-optimal design for timing-constrained cnns. CASES – TCAD, 2018.
[8] Xiaofan Zhang, et al. Dnnbuilder: an automated tool for building high-performance dnn hardware accelerators for fpgas. In ICCAD, 2018.
[9] Weiwen Jiang, et al. Xfer: A novel design to achieve super-linear performance on multiple fpgas for real-time ai. In FPGA 2019.
Implementing Fixed NNs on FPGAs
Notes: However, these works are most for fixed neural arch for FPGA, not about searching for the best neural networks