## Slide 1: Hardware/Software Co-Exploration of Neural Architecture —— Published and Ongoing Works
Weiwen Jiang
wjiang2@nd.edu

## Slide 2
1
Introduction
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC’19 (Best Paper Nomination)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 3
Computation Gap
Performance density almost stops increasing
2
Number of DNN operations increases exponentially
[ref.1] Xu, Xiaowei, et al. "Scaling for edge inference of deep neural networks." Nature Electronics 1.4 (2018): 216.
[ref.2] Sutter, H. The free lunch is over: A fundamental turn toward concurrency in software. Dr Dobb’s J. 30, 202–210.

## Slide 4
Storage Gap
[ref.1] Xu, Xiaowei, et al. "Scaling for edge inference of deep neural networks." Nature Electronics 1.4 (2018): 216.
[ref.2] Sutter, H. The free lunch is over: A fundamental turn toward concurrency in software. Dr Dobb’s J. 30, 202–210.
Number of DNN parameters increases exponentially
Energy efficiency of memory almost stops increasing

## Slide 5
Real-Time Requirement
[ref.1] Google’s Waymo
[ref.2] da Vinci Surgical Robot at St. Francis Health Center - Robotic Gizmos
Self-Driving Vehicle
Traffic Surveillance
Increasing Demands on Real-Time Machine Learning Applications
Robots in Surgery

## Slide 6
5
5
Neural Architecture Search
Neural Architecture Implementation on Hardware
Efforts on Both Software and Hardware Sides are Demanded
—— Hardware Implementation and Optimization
Notes: Page 6:
Now, let’s move our eyesight to the other side of the bridge. I will introduce the progress of neural architecture search in the following.

## Slide 7
FPGAs in DNN Applications
FPGA in Cloud Computing
[ref] Where Do FPGAs Stand in Auto IC Race? https://www.eetimes.com/document.asp?doc_id=1333419#
[ref] PYNQ on UAV http://brennancain.com/pynqcopter-an-open-source-fpga-overlay-for-uavs/
FPGA in Edge Computing
Notes: The workflow of deploying neural architecture on FPGA consists FPGA accelerator design, the HDL code generation, synthesis, place and routing, and hardware performance evaluation. Among these steps, in accelerator design and HDL code generation, hardware design knowledge is mandatory (click) . And for synthesis, and place&routing, (click)it can take dozens of hours. Such lengthy development can be an obstacle when Deploying Neural Architecture on FPGA. (click)

## Slide 8
[1] Chen Zhang, et al. Optimizing fpga-based accelerator design for deep convolutional neural networks. In FPGA, 2015.
[2] Chen Zhang, et al. Energy-efficient cnn implementation on a deeply pipelined fpga cluster. In ISLPED, 2016.
[3] Chen Zhang, et al. Caffeine: Towards uniformed representation and acceleration for deep convolutional neural networks. ICCAD, 2016.
[4] Yongming Shen, et al. Maximizing cnn accelerator efficiency through resource partitioning. In ISCA, 2017.
[5] Eric Chung, et al. Serving dnns in real time at datacenter scale with project brainwave. IEEE Micro, 2018.
[6] Jeremy Fowers, et al. A configurable cloud-scale dnn processor for real-time ai. In ISCA, 2018.
[7] Weiwen Jiang, et al. Heterogeneous fpga-based cost-optimal design for timing-constrained cnns. CASES – TCAD, 2018.
[8] Xiaofan Zhang, et al. Dnnbuilder: an automated tool for building high-performance dnn hardware accelerators for fpgas. In ICCAD, 2018.
[9] Weiwen Jiang, et al. Xfer: A novel design to achieve super-linear performance on multiple fpgas for real-time ai. In FPGA 2019.
Implementing Fixed NNs on FPGAs
Notes: However, these works are most for fixed neural arch for FPGA, not about searching for the best neural networks

## Slide 9
8
8
Neural Architecture Search
Neural Architecture Implementation on Hardware
Efforts on Both Software and Hardware Sides are Demanded
—— Neural Architecture Design
Notes: To maximize the energy efficiency, starting from 2015, a lot of works are carried out to implement a fixed architecture on FPGA.
However, with the growing demands on real-time AI, it is more critical to improve the timing performance of FPGA accelerators, which are usually bounded by the limited resource on one FPGA.
To response to this problem, there is trend to involve multiple FPGAs to implement deep neural networks.
But, it still lacks a design to efficiently utilize multiple FPGAs. Our transfer work aims to address this problem.
On the other hand, in the last 2 years, there are sharply increasing number of works targeting on neural architecture search. This has already become a very hot topic.
However, there is still a missing link between the neural architecture search and FPGA-implementation, so how do we search for neural architecture that works best for FPGA is still unknown.
Our FNAS work aims to propose a co-exploration framework to fill this gap.
In the following, I’ll introduce the backgrounds on FPGA-implementation side and Neural Architecture Search side in turn.

## Slide 10
2013
2012
2014
2015
2016
2017
2018
2019
AlexNet
GoogLeNet
VGGNet
ZFNet
2020
I. Human
Invented
II. Pure Automatically Explore Neural Architecture Space
III. Hardware-Aware
Neural Architecture Search
2018.Nov
proxylessNAS
from MIT
2018.Dec
FBNet
from UCB & Facebook
2019
2018.July
MnasNet
from Google
Neural Architecture Search (RL-based)
Evolution of Exploring Deep Neural Architectures
Notes: We can divide the evolution of exploring neural architectures in four stages.
The first stage is human invented stage, in which neural architectures are manually explored by experts, however, it requires large expertise and labor. (click)
Then, in the second stage, neural architecture search algorithms is proposed to automatically identify architectures. It release the expertise but can easily become useless since their structures are too complicated and cannot satisfy the timing performance. (click)
The third stage is the hardware-aware neural architecture search, which involve the hardware-efficiency in the search loop. (click)
Finally, our FNAS work pushes the exploration to the fourth stage, which will co-explore neural architecture and hardware design.
In the following slides, I will introduce each stage in detail and show the motivation of the co-exploration.

## Slide 11
VGGNet
AlexNet
……
Domain knowledge and excessive labor
It is impossible to manually design specific arch. for dedicated application in the era of AI democratization
Problem
Design arch. for dedicated application
Era of AI Democratization
Phase I: Human Invented
Notes: In the first stage, the neural network architectures are designed for the dedicate applications and dataset; for instance, the AlexNet and VGGNet are designed for image classification application on ImageNet dataset. (click)
However, when it comes to the era of AI democratization, there are exponentially growing number of applications. As a result, it is impossible to manually design architectures for each application.

## Slide 12
Intelligent Edge with Limited Computing Power
Controller (RNN)
Train a child network with architecture
NN to get accuracy A
Sample architecture NN with probability p
Compute gradient of p and scale it by A to update the controller
REF: Zoph, Barret, and Quoc V. Le. "Neural architecture search with reinforcement learning." ICLR 2017
before convergence
after convergence
Intelligent Cloud
with Enough Computing Power
No constraint on hardware resource consumed
NAS may not meet the design specifications in resource constraint environment
Problem
Identified
NN
Phase II: Neural Architecture Search (NAS)
Notes: In such background, the neural architecture search algorithms are proposed to automatically identify the architecture.
The NAS is typically implemented as a search loop, which composed of two components: a controller and a trainer.
The controller will predict the hyperparameters to identify an architecture. And the architecture will be then trained from scratch to obtain the accuracy. Then the accuracy will be feedback to update controller with the objective of maximizing the accuracy. (click)
We observe that the network explored by NAS has complicated structures, which is fine for the cloud computing with enough computing power. (click)
But, when it comes to edge computing, which commonly has limited resource and tight hardware specifications (such as latency and throughput), if we directly implement the identified architectures onto the edge devices, it is easily violate the specification and result in the architecture useless.

## Slide 13
Controller (RNN)
Train a child network with architecture
NN to get accuracy A
Sample architecture NN with probability p
Compute gradient of p and scale it by A and E to update the controller
REF: Mingxing Tan, et al. "MnasNet: Platform-Aware Neural Architecture Search for Mobile.” arXiv 2018
Predict the efficiency E on a fixed hardware (e.g. mobile phone)
It works for particular fixed hardware, but not suitable for programmable hardware
Problem
Different Hardware Designs
Phase III. Hardware-Aware NAS
Notes: To solve this problem, hardware-aware NAS is proposed, which adds an extra component in the search loop as shown in this slide.
It will test the hardware efficiency after training the neural network. (click)
In this way, the hardware efficiency can be guaranteed, but it increases the latency of search process. (click)
What’s more, it only works for fixed hardware, but not suitable for the programmable hardware.

## Slide 14
A Missing Link between Two Design Spaces
Neural Architecture Search
Neural Architecture Implementation on Hardware
Notes: Although two design spaces have been well explored, there is a missing link between these two spaces.
What’s more, we observe that these two spaces are tightly coupled, separately optimization will lead to inferior solutions.
Therefore, it is best to jointly explore these two spaces.
FNAS is proposed to remedy this gap.

## Slide 15
2013
2012
2014
2015
2016
2017
2018
2019
AlexNet
GoogLeNet
VGGNet
ZFNet
2020
I. Human
Invented
II. Pure Automatically Explore Neural Architecture Space
III. Hardware-Aware
Neural Architecture Search
2018.Nov
proxylessNAS
from MIT
2018.Dec
FBNet
from UCB & Facebook
2019
2018.July
MnasNet
from Google
Neural Architecture Search (RL-based)
DAC19 FNAS
from ND
IV. Co-Explore Neural Architecture Space
and Hardware Design Space
……
Evolution of Exploring Deep Neural Architectures
Notes: We claim that, the proposed FNAS pushes the neural architecture evolution into the fourth stage, that is, co-exploration stage.

## Slide 16
15
Introduction
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC 2019 (Best Paper Nomination)
Other Research Directions
Conclusion
Outline

## Slide 17
FNAS Framework

## Slide 18
Output: A pair of neural architecture and hardware design
FNAS
HW-Aware NAS vs. FPGA-Implementation Aware NAS（FNAS）
Output: A neural architecture
HW-Aware NAS
Notes: We first show the difference between the co-exploration framework with the existing hardware-aware NAS.
As stated, the hardware-aware NAS integrated a component to test the accuracy for each child network. It finally outputs a neural architecture with high accuracy. (click)
Unlike this framework, our proposed co-exploration framework is composed of two levels of exploration.
The top layer shows the hardware exploration level, and the bottom layer shows the software exploration level.
There are two controllers cooperatively explore neural architecture and hardware implementation.
As shown in this slides, after the controller for maximizing accuracy generate a child network, our framework can also test its hardware efficiency. If it cannot meet specifications, we can terminate the training early to reduce search time. Otherwise, it applies the latency and accuracy together to update the controller.
Then, the parameters of the controller is copied to the other controller. And it optimizes the hardware implementation with the objective of maximizing hardware efficiency.

## Slide 19
Naïve Solution: HW-Aware + Exhaustively Evaluate Lat.
Challenges:
Functional Spec.
HDL
Synthesis
Place & Route
HW Evaluation
Fig2. Procedure of performance evaluation
C3: Time-consuming evaluation!
Our Solution: FNAS tools to response to challenges
C2: Multi-FPGA design!
C1
C2
C2
C3
Fig1. Possible designs for Layer 5 of AlexNet on ZCU102
C1: Huge design space!
Infeasible
Solutions & Challenges
Exhaustively
Evaluate
Latency
FNAS
Tool
Notes: The naïve solution is to apply hardware-aware approach and exhaustively evaluate performance.
However, it faces a lot of challenges which leads such approach infeasible.
First, it has huge design space. As shown in the figure, each point in the graph represent one possible design, and the design space is huge.
Second, when we consider multiple FPGAs, the design space increases exponentially.
Finally, if we do not have automatic approach to evaluate performance, it is time-consuming.
To address these challenges, we propose the FNAS toolset, which contains four components.

## Slide 20
REF: Chen Zhang et al. 2015. Optimizing fpga-based accelerator design for deep convolutional neural networks. In Proc. of FPGA.
1. FPGAs with attributes including LUTs, DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
On-chip accelerator design:
1. On-chip buffer allocation; 2. Accelerator size for computing
(note: both are determined by tiling parameters, Tm, Tn, Tr, Tc)
Determine：
One layer:
Multiple layers:
FNAS: Design Optimization (on-chip design)
Tn/Tm
Tn/Tm
Notes: The first component is the FNAS-Design. It determine the on-chip buffer size, and accelerator size.
These parameters are affected by tiling parameters. And we have an automatic algorithm to help to determine best parameters given an architecture.

## Slide 21
High-level graph abstraction
1. FPGAs with attributes including LUTs, DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
FNAS: Graph Generator
Notes: The second component is the graph generator. It bases the tiling results to abstract a graph model for the neural network.

## Slide 22
1. FPGAs with attributes including LUTs, DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
Schedule of tasks in graph on multiple FPGAs
FNAS: Schedule (off-chip design)
Notes: Based on the graph model, we build a scheduler to determine the execution order of each operation.

## Slide 23
Latency = pipeline start time + processing time
1. FPGAs with attributes including LUTs, DSPs, BRAM, etc.
2. A neural architecture with determined hyperparameters
……
Given：
1. A tailored FPGA Design
2. The system latency
Output：
FNAS: Analyzer
Notes: Finally, we based on our FPGA performance model studied in the previous work to efficiently analyze the performance without simulation.

## Slide 24
Experimental Results
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 25
MNIST
CIFAR-10
ImageNet
Datasets
NAS Search Space
Layer Num.
Filter Size
Filter Num.
Channel Tiling Para. (Tm,Tn); Row Tiling Para. (Tr); Col Tiling Para. (Tc); Schedule
up to 5
up to 10
up to 15
[5, 7, 14]
[1, 3, 5, 7]
[1, 3, 5, 7]
[9, 18, 36]
[24, 36, 48, 64]
[16, 32, 64, 128]
[2, 5, 10, 20]
[1.5, 2, 2.5, 10]
[2.5, 5, 7.5, 10]
FPGAs
Xilinx 7A50T
Xilinx 7Z020
HW Search Space
Timing Spec. (ms)
Experimental Setting
Notes: In the experiments, we use different FPGAs to composed the hardware design space.
For the architecture search space, we specify number of layers, filter sizes, and filter numbers for different dataset, including MNIST, CIFAR-10 and ImageNet.
We also test using different timing specifications.

## Slide 26
up to 11.13X reduction in search time
up to 7.81X reduction in inference latency
below 0.9% loss in accuracy
Different Hardware (CIFAR-10)
Different Datasets (7Z020)
Compare to HW-Aware NAS
(CIFAR-10 + 7Z020)
FNAS can significantly push forward the Pareto frontiers between accuracy and efficiency tradeoff
below 1% loss in accuracy
up to 10X reduction in inference latency
Baseline: NAS
loose
Experimental Results
Notes: We conduct experiments on different hardware and datasets. We also compare FNAS with original NAS and hardware-aware NAS.
As shown in the first group of experiments, where the x-axis represent different FPGAs, and y-axis represent search time, latency, and accuracy. We can see that FNAS can achieve 11 times reduction on search time, and 7 times reductions on latency, with only 0.9 percent accuracy loss.
For different datasets, we can obtain similar results.
Finally, we show that FNAS can significantly push forward the Pareto frontiers between accuracy and efficiency tradeoff.

## Slide 27
Experimental Results: Superior to Existing Approaches
Optimizing Network Accuracy
Comparison the proposed Co-Exploration with Hardware-Aware NAS and Heuristic Sequential Optimization
n
Optimizing Hardware Efficiency

## Slide 28
Experimental Results: Importance of Co-Exploration
Model Size
149k ~ 150k
Hardware Efficiency
7.02% ~ 98.53%
In the design space:
Models with similar model sizes may have distinct hardware efficiency
=> Cannot restrict model size to guarantee hardware efficiency

## Slide 29
28
Introduction
Co-Exploration of Neural Architecture and FPGA Implementation
- DAC 2019 (Best Paper Nomination)
Other Research Directions
Conclusion
Outline
Notes: Page 1:
My talk will be composed of four parts.
First, I will brefiely introduce the background of these works.
Then, I’ll present two recent works. The first one is transfer, which is a design to achieve super-linear performance of convolutional neural networks across Multiple FPGAs. This work is just accepted by CODES+ISSS.
The second one is FNAS, which is a framework to support co-exploration of Neural Architectures and FPGA implementations.
Finally, I’ll conclude this talk.

## Slide 30
29
29
Our Work on Co-Exploring Neural Architecture and Hardware
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)

## Slide 31
30
30
Our Work on Co-Exploring Neural Architecture and Hardware
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Limited Resource in Edge Computing (quantization, etc.)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
……

## Slide 32
31
31
Design Neural Networks on Scalable Architecture
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Super-Linear Speedup across Multiple FPGAs (XFER)
CODES+ISSS’19
Best Paper Nomination

## Slide 33
[Ref] C. Zhang et al. Optimizing fpga-based accelerator design for deep convolutional neural networks. In Proc. of FPGA, pages 161–170. ACM, 2015.
Single-FPGA
Limited Resource  Limited Performance
[Ref] C. Zhang et al. Energy-efficient cnn implementation on a deeply pipelined fpga cluster. In Proc. of ISLPED, pages 326–331, 2016.
Pipelined FPGAs
Pipeline High Throughput
Latency is not improved
MS Brainwave
Lock weights to multiple FPGAs  Specific for RNN
Not applicable for sharing weights (e.g. CNN)
[Ref] Eric Chung, et al. Serving DNNs in Real Time at Datacenter Scale with Project Brainwave, In IEEE Micro, 2018
Existing Implementations
Notes: Page 14:
Let’s first review the existing designs.
As shown in this slides, the very early implementation on single FPGA cannot satisfy the real-time requirements due to the limited resource. (click)
Then, the multiple FPGA solution is proposed to form a pipeline. Such structure is able to improve throughput, but cannot reduce latency. (click)
Most recently, Microsoft Brainwave project proposed to lock weights of RNN onto multiple FPGAs to avoid loading weights from off-chip memory. It can only work for specific neural networks, but not applicable for the commonly used convolutional neural network, where weights need to be shared.
In the XFER work, we are going to explore a more general design that can accelerate convolutional neural networks on multiple FPGAs.

## Slide 34
XFER: Architecture and Motivation
FPGA 1
FPGA 2
Different clock domains for computation (low) and communication (high)
Communication not go through Off-Chip Memory, but directly switch between on-chip buffers
Feature
Results & Motivations
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 35
Performance on Single FPGA bounded by Limited Resource
FPGA 1
FPGA 2
IFM
Weights
OFM
NN | Operation | Cycles | Note
AlexNet Layer 5 | Comm_IFM | 2,612 | Performance Dominated by Comm_Weights Latency is 5,658
 | Comm_Weights | 5,658 | 
 | Comm_OFM | 368 | 
 | Computation | 3,326 | 
K times
(in terms of tiling parameters)
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 36
FPGA 1
FPGA 2
Double Computation Resource cannot Double Performance
NN | Operation | Single | w/o XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 |  | 
 | Comm_Weights | 5,658 |  | 
 | Comm_OFM | 368 |  | 
 | Computation | 3,326 |  | 
Partition
for
Parallel
w/o XFER
1,412
2,953
234
1,782
IFM
Weights
OFM
K times
(in terms of tiling parameters)
Note
1.91X Speedup
times
(K is in terms of tiling parameters)
(m is in terms of stride and padding)
Loading IFM, OFM, Computation are conducted independently on two FPGAs
Performance is still dominated by loading weights, and weights are duplicated on two FPGAs
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 37
FPGA 1
FPGA 2
XFER: Achieve Super-Linear Speedup by Transferring Accesses —— from Off-Chip Memory to Inter-FPGA Links
NN | Operation | Single | w/o XFER | w/ XFER | Note
AlexNet Layer 5 | Comm_IFM | 2,612 | 1,412 |  | 
 | Comm_Weights | 5,658 | 2,953 |  | 
 | Comm_OFM | 368 | 234 |  | 
 | Computation | 3,326 | 1,782 |  | 
XFER
Further Partition
Weights
Note
Bottleneck Moves to Comp. 3.18X Speedup
w/ XFER
1,412
1,695
234
1,782
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 38
Experimental Results
Testbed:
Xilinx ZUC102 FPGAs connected by SFP+ Links
XFER
Lowest
Latency
among all
competitors
Comparison results of XFER with comparisons to GPUs and the existing FPGA designs
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 39
Experimental Results
Comparison results of XFER with SOTA single FPGA design
Achieve Super-Linear Speedup for both 32-bits and 16-bits implementations
Notes: With FNAS, the neural architecture search evolves to another higher stage.

## Slide 40
39
39
Design Neural Networks on Scalable Architecture
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Super-Linear Speedup across Multiple FPGAs (XFER)
CODES+ISSS’19
Best Paper Nomination
ASP-DAC’20
Best Paper Nomination
Co-Explore Network-on-Chip Design and Neural Architectures (NANDS)

## Slide 41
NANDS: Co-Explore NoC Design and Neural Architectures
D
Why NoC? Complicated Structure from NAS
Fixed design (X-Y routing) leads lower performance
31.37% Improvement
D
Co-Exploration Framework
Results

## Slide 42
41
41
Design Neural Networks for Resource-Limited Device
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Limited Resource in Edge Computing (quantization, etc.)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
……

## Slide 43
42
42
Design Neural Networks for Resource-Limited Device
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Limited Resource in Edge Computing (quantization, etc.)
ICCAD’19
Co-Explore Quantization and Neural Architectures (QuanNAS)

## Slide 44
D,E,F are explored by our Co-Exploration framework, which output
QuanNAS: Co-Explore Quantization and Neural Architectures
D
Search Space
Besides filter size and shape, we co-explore bit width of weights and activation data, for FPGAs and ASICs.
D
Results
A,B are first explored by NAS, then to be quantized. In this way, the accuracy loss by quantization is huge.
D,E,F are explored by our Co-Exploration framework, which output better accuracy for quantized network with smaller parameter size

## Slide 45
44
44
Design Neural Networks for Novel Computing Architectures
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Scalability in Cloud Computing (multiple-FPGAs, NoCs, etc.)
Limited Resource in Edge Computing (quantization, etc.)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
……

## Slide 46
45
45
Design Neural Networks for Novel Computing Architectures
DAC’19 Best Paper Nomination
FPGA Implementation-Aware NAS
(FNAS)
Novel Computing Architectures (in-memory Computing, NVM, etc.)
Integrating Memristors and CMOS for Better AI
Nature Electronics’19
Submitted to TC
Co-Explore Neural Architectures and Devices

## Slide 47
46
Introduction
Co-Explore Neural Architecture and FPGA Implementation
- DAC 2019 (Best Paper Nomination)
Research Directions
Conclusion
Outline

## Slide 48
Conclusion and Future Work
FNAS
Neural Network
Architecture
Search
Large Scale System
for Real-Time AI
FNAS
AI Democratization
XFER
NANDS
QuanNAS
?
?
New
Architectures
(ASIC, NVM, …)

## Slide 49
48
[1] Weiwen Jiang, Xinyi Zhang, Edwin H.-M. Sha, Qingfeng Zhuge, Lei Yang, Yiyu Shi and Jingtong Hu, "Accuracy vs. Efficiency: Achieving Both through FPGA-Implementation Aware Neural Architecture Search," in Proc. of DAC 2019. (Nominated for Best Paper Award)
[2] Weiwen Jiang, Edwin Sha, Xinyi Zhang, Lei Yang, Qingfeng Zhuge, Yiyu Shi and Jingtong Hu, "Achieving Super-Linear Speedup across Multi-FPGA for Real-Time DNN Inference," CODES+ISSS 2019 and ACM TECS (Nominated for Best Paper Award)
[3] Lei Yang, Weiwen Jiang, Weichen Liu, Edwin Sha, Yiyu Shi and Jingtong Hu, "Co-Exploring Neural Architecture and Network-on-Chip Design for Real-Time Artificial Intelligence," ASP-DAC 2020 (Nominated for Best Paper Award)
[4] Qing Lu, Weiwen Jiang, Xiaowei Xu, Yiyu Shi and Jingtong Hu, "On Neural Architecture Search for Resource-Constrained Hardware Platforms," in Proc. of ICCAD 2019 (Invited Paper)
[5] Weiwen Jiang, Bike Xie, Chun-Chen Liu and Yiyu Shi, "Integrating Memristors and CMOS for Better AI," Nature Electronics, September 2019
Reference

## Slide 50: Thank You!